## Slide 1: 邊緣人工智慧 Edge AI
Basics of Artificial Intelligence (AI) and Deep Learning (DL)
吳凱強
Kai-Chiang Wu

## Slide 2: Deep Learning Continues to Scale
The demand of computation grows exponentially
100
10
1
0.1
0.01
1000
2017
2018
2020
2021
2022
Model Size (#Params in Billion)
2
MT-NLG
 |  | GPT-3 175B | 530B
 |  | T-NLG 17B | 
 | Me | gatronLM 8.3B | 
 | GPT-2 1.5B BERT |  | 
GP Transformer 0. 0.05B | 0.34B T 11B | As | Model Size sume data are FP16.

## Slide 3: Problem: DL Models Outgrow Hardware
Moore’s Law: 2x every 2 years; DL models: 4x every 2 years
0.01
3
0.1
1
10
100
1000
2017
2018
2020
Model Size GPU Memory
GPT 0.11B
MegatronLM 8.3B
GPT-2 1.5B
Model Size (#Params in Billion)
BERT
0.34B
Transformer 0.05B
GPT-3 175B
MT-NLG
530B
T-NLG 17B
TPUv2 16GB
V100 32GB
TPUv3 32GB
A100 40GB
A100 80GB
Assume data are FP16.
2021 2022

## Slide 4: Efficient Deep Learning Techniques are Essential
Bridges the gap between the supply and demand of computation
0.01
0.1
1
10
100
1000
2017
2018
2020
Model Size GPU Memory
GPT 0.11B
MegatronLM 8.3B
GPT-2 1.5B
Model Size (#Params in Billion)
BERT
0.34B
Transformer 0.05B
GPT-3 175B
MT-NLG 530B
T-NLG 17B
TPUv2 16GB
V100 32GB
TPUv3 32GB
A100 40GB
A100 80GB
Assume data are FP16.
2021 2022
4
Model compression bridges the gap.

## Slide 5: Lecture Plan
Review the terminology of neural networks
Review popular building blocks in a neural network
Review convolutional neural networks’ architecture
Introduce popular efficiency metrics for neural netowrks

## Slide 6: Neuron and Synapse
Synapse
Cell Body
Axon
Dendrite
Synaptic Terminals
Impulse
Activation Function
Cell Body
Output Axon
Synapse
Input Axon
Dendrite

## Slide 7: Deep Neural Network
Neurons / Features / Activations
Synapses / Weights / Parameters
Layer 0
Hidden Layer 1
Hidden Layer 2
Inputs
Outputs
The dimensionality of these hidden layers determines the width of the model.
Activation Function
Cell Body
Output Axon
Synapse
Input Axon
Dendrite
3-Layer Neural Network With 2 Hidden Layers

## Slide 8: Popular Neural Network Layers

## Slide 9: Fully-Connected Layer (Linear Layer)
y2
y1
y0
x4
x3
x0 x1 x2
w
00
w
42
co
ci
=
co
WT
X
Y
ci
Notations | 
ci | Input Channels
co | Output Channels
The output neuron is connected to all input neurons.
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 10: Fully-Connected Layer (Linear Layer)
WT
X
Y
co
ci
= n
co
ci
n
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
y2
y1
y0
x4
x3
x0 x1 x2
w
00
w
42
The output neuron is connected to all input neurons.
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 11: Fully-Connected Layer (Linear Layer)
WT
X
Y
co
ci
= n
co
ci
n
y2
y1
y0
x4
x3
x0 x1 x2
w
00
w
42
z
z
0 1
Multilayer Perceptron (MLP)
The output neuron is connected to all input neurons.
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels

## Slide 12: Convolution Layer
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)
.
channel dimension
spatial dimension(s)
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
1D Conv
(n=1, ci, wi)
(n=1, co, wo)

## Slide 13: Convolution Layer
.
channel dimension
spatial dimension(s)
kw
c
i
Filter
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
kw | Kernel Width
1D Conv
(n=1, ci, wi)
(n=1, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 14: Convolution Layer
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
kw | Kernel Width
channel dimension
spatial dimension(s)
kw
c
i
Filter
1D Conv
(n=1, ci, wi)
(n=1, co, wo)
(co, ci, kw)

## Slide 15: Convolution Layer
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
kw | Kernel Width
channel dimension
spatial dimension(s)
kw
c
i
Filter
co
1D Conv
(n=1, ci, wi)
(n=1, co, wo)
(co, ci, kw)

## Slide 16: Convolution Layer
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
kw | Kernel Width
1D Conv
(n=1, ci, wi)
(n=1, co, wo)
(co, ci, kw)

## Slide 17: Convolution Layer
channel dimension
spatial dimension(s)
kw
ci
co
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
kw | Kernel Width
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)
1D Conv
(n=1, ci, wi)
(n=1, co, wo)
(co, ci, kw)

## Slide 18: Convolution Layer
.
spatial dimension(s)
Activation Map / Feature Map
hw
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
channel dimension
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 19: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
channel dimension
spatial dimension(s)
kw
Filter
kh
ci
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 20: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
channel dimension
spatial dimension(s)
kw
Filter
kh
ci
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 21: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
channel dimension
spatial dimension(s)
kw
Filter
kh
ci
co
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 22: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
channel dimension
spatial dimension(s)
co
Weight Sharing
hi
wo
ho
wi
kw
kh
ci
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 23: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
hi
wo
ho
channel dimension
spatial dimension(s)
co
wi
kw
kh
ci
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 24: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
hi
wo
ho
wi
spatial dimension(s)
channel dimension
spatial dimension(s)
ci
co
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 25: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
hi
wo
ho
wi
channel dimension
spatial dimension(s)
ci
co
Image source: 1
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 26: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
hi
wo
ho
wi
spatial dimension(s)
channel dimension
spatial dimension(s)
ci
co
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 27: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
hi
wo
ho
wi
channel dimension
ci
co
Image source: 1
spatial dimension(s)
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 28: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
hi
wo
ho
wi
channel dimension
spatial dimension(s)
ci
co
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 29: Convolution Layer
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
hi
wo
ho
wi
channel dimension
spatial dimension(s)
ci
co
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)

## Slide 30: Convolution Layer
The output neuron is connected to input neurons in the receptive field
  Shape of Tensors:
    Input Features X : (n, ci)
    Output Features Y : (n, co)
    Weights W : (co, ci)
    Bias b : (co)
.
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
hi
wo
ho
wi
channel dimension
spatial dimension(s)
kw
kh
ci
co
Image source: 1
Feature map size becomes smaller.
2D Conv
(n=1, ci, hi, wi)
(co, ci, kh, kw)
(n=1, co, ho, wo)
1D Conv
(n, ci, wi)
(n, co, wo)
(co, ci, kw)

## Slide 31: Convolution Layer: Padding
Padding can be used to keep the output feature map size is the same as input feature map size
  Zero Padding pads the input boundaries with zero.
  Other Paddings: Reflection Padding, Replication Padding, Constant Padding
h
i
w
i
wo
h
o
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 2 | 3 | 0 | 0
0 | 0 | 4 | 5 | 6 | 0 | 0
0 | 0 | 7 | 8 | 9 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
9 | 8 | 7 | 8 | 9 | 8 | 7
6 | 5 | 4 | 5 | 6 | 4 | 5
3 | 2 | 1 | 2 | 3 | 2 | 1
6 | 5 | 4 | 5 | 6 | 5 | 4
9 | 8 | 7 | 8 | 9 | 8 | 7
6 | 5 | 4 | 5 | 6 | 5 | 4
3 | 2 | 1 | 2 | 3 | 2 | 1
1 | 1 | 1 | 2 | 3 | 3 | 3
1 | 1 | 1 | 2 | 3 | 3 | 3
1 | 1 | 1 | 2 | 3 | 3 | 3
4 | 4 | 4 | 5 | 6 | 6 | 6
7 | 7 | 7 | 8 | 9 | 9 | 9
7 | 7 | 7 | 8 | 9 | 9 | 9
7 | 7 | 7 | 8 | 9 | 9 | 9
Zero Padding
Reflection Padding
Replication Padding
hi = wi = 5 kh = kw = 3 ho = wo
= 5 + 2 × 1 − 3 + 1
= 5
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
p is padding
ho = hi + 2p − kh + 1

## Slide 32: Convolution Layer: Receptive Field
  In convolution, each output element depends on khkw receptive field in the input
  Each successive convolution adds k1 to the receptive field size
  With L layers, the receptive field size is
Problem: For large images, we need many layers for each output to “see” the whole image Solution: Downsample inside the neural network
36

## Slide 33: Strided Convolution Layer

## Slide 34: Grouped Convolution Layer
A group of narrower convolutions
  Shape of Tensors:
    Input Features X : (n, ci, hi, wi)
    Output Features Y : (n, co, ho, wo)
    Weights W : (co, ci, kh, kw)
    Bias b : (co)
co
c
i
co
c
i
g = 2
g = 1
(g ⋅ co/g, ci/g, kh, kw)
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
g | Groups
channel

## Slide 35: Depthwise Convolution Layer
Independent filter for each channel: g = ci = co in grouped convolution
  Shape of Tensors:
    Input Features X : (n, ci, hi, wi)
    Output Features Y : (n, co, ho, wo)
    Weights W : (co, ci, kh, kw)
    Bias b : (co)
(ci, kh, kw)
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh | Kernel Height
kw | Kernel Width
g | Groups
co
c
i

## Slide 36: Pooling Layer
Downsample the feature map to a smaller size
  The output neuron pools the features In the receptive field, similar to convolution.
    Usually, the stride is the same as the kernel size: s = k
  Pooling operates over each channel independently
    No learnable parameters
5 | 0 | 1 | 7
2 | 1 | 3 | 5
0 | 2 | 3 | 1
2 | 8 | 1 | 3
5 | 7
8 | 3
2 | 4
3 | 2
stride = kernel size = 2
Input Feature Map
Output Feature Map
Max Pooling
Average Pooling

## Slide 37: Normalization Layer
Normalizing the features makes optimization faster.
  Normalization layer normalizes the features as follows,
    is the mean, and is the standard deviation (std) over the set of pixels 𝒮I
  Then learns a per-channel linear transform to compensate for the possible lost of representational ability
h × w
h × w
h × w
channel dim
spatial dim
h × w
batch dim
Group Norm
Different normalizations use different definitions of the set 𝒮i
(color in the blue)
Instance Norm
Layer Norm
Batch Norm

## Slide 38: Activation Function
Activation functions are typically non-linear functions
-10
0
10
-10 0 10
-5
0
5
-5 0 5
-10
0
10
-10 0 10
-5
0
5
-5 0 5
-1
0
1
-10 0 10
-5
0
5
Sigmoid
ReLU
ReLU6
y = 1/ (1 + e−x)
y = max (x, x)
Leaky ReLU
Swish
y = x / (1 + e−x)
Activation Function
Cell Body
Output Axon
Synapse
Input Axon
Dendrite
y = max (0, x)
y = min(max (0, x), 6)
Other Activation Functions: Tanh, GELU, ELU, Mish…
-5 0 5
Hard Swish

## Slide 39: Popular Neural Network

## Slide 40: AlexNet
w
i
wo
h
o
Convolution Layer / Pooling Layer
hi
WT
X
Y
co
ci
= n
co
ci
n
Linear Layer
p is padding
s is stride

## Slide 41: VGG 16
w
i
wo
h
o
Convolution Layer / Pooling Layer
hi
WT
X
Y
co
ci
= n
co
ci
n
Linear Layer
p is padding
s is stride

## Slide 42: ResNet-50
48

## Slide 43: MobileNetV2

## Slide 44: Efficiency Metrics
How should we measure the efficiency of neural networks?

## Slide 45: Efficiency of Neural Networks
Faster
Smaller
Greener
Efficiency Metrics

## Slide 46: Efficiency of Neural Networks
Faster
Smaller
Greener
Storage
Latency
Energy
Computation
Memory
Efficiency Metrics
Memory-Related #parameters
model size
total/peak #activations
Computation-Related
MAC
FLOP, FLOPS
OP, OPS

## Slide 47: Latency
Measures the delay for a specific task
Speed is measured on Nvidia Jetson AGX Orin with TensorRT, fp16, batch size 1.
High Latency 638ms
Low Latency 46ms

## Slide 48: Throughput
Measures the rate at which data is processed
Low Throughput = 6.1 video/s
High Throughput = 77.4 video/s

## Slide 49: Latency vs. Throughput
Does higher throughput translate to lower latency? Why?
Does lower latency translate to higher throughput? Why?
50 ms
50 ms
100 ms
100 ms
100 ms
100 ms
Design 2
Latency: 100 ms
Throughput: 40 image/s
Design 1
Latency: 50 ms
Throughput: 20 image/s

## Slide 50: Latency
Load Input
Load Weight
Store Output
Compute |  |  | Store Output | 
Load Input | Load Weight |  | Compute | 
t
Data Movement and Computation can be overlapped.
Hardware Specification
NN Specification
Number of Operations in Neural Network Model
Neural Network Model Size NN Specification
Latency ≈ max (Tcomputation, Tmemory)
Tcomputation ≈
Number of Operations that Processor can Process Per Second
Hardware Specification
Tdata movement of weights ≈
Memory Bandwidth of Processor
Tmemory ≈ Tdata movement of activations + Tdata movement of weights
NN Specification
Input Activation Size + Output Activation Size
Tdata movement of activations ≈
Memory Bandwidth of Processor Hardware Specification

## Slide 51: Energy Consumption
Data movement → more memory reference → more energy
Operation | Energy [pJ]
32 bit int ADD | 0.1
32 bit float ADD | 0.9
32 bit Register File | 1
32 bit int MULT | 3.1
32 bit float MULT | 3.7
32 bit SRAM Cache | 5
32 bit DRAM Memory | 640
10
100 1000 10000
Rough Energy Cost For Various Operations in 45nm 0.9V
Relative Energy Cost
200 ✕
1
= 200
1

## Slide 52: Energy Consumption
Data movement → more memory reference → more energy
1
10
100 1000 10000
Rough Energy Cost For Various Operations in 45nm 0.9V
Relative Energy Cost
200 ✕
Operation | Energy [pJ]
32 bit int ADD | 0.1
32 bit float ADD | 0.9
32 bit Register File | 1
32 bit int MULT | 3.1
32 bit float MULT | 3.7
32 bit SRAM Cache | 5
32 bit DRAM Memory | 640

## Slide 53: Efficiency of Neural Networks
Faster
Smaller
Greener
Storage
Latency
Energy
Computation
Memory
Image source: 1
https://eﬃcientml.ai
Efficiency Metrics
Memory-Related #parameters
model size
total/peak #activations
Computation-Related
MAC
FLOP, FLOPS
OP, OPS

## Slide 54: Efficiency of Neural Networks
Faster
Smaller
Greener
Storage
Latency
Energy
Computation
Memory
Image source: 1
https://eﬃcientml.ai
Efficiency Metrics
Memory-Related #parameters
model size
total/peak #activations
Computation-Related
MAC
FLOP, FLOPS
OP, OPS

## Slide 55: Number of Parameters (#Parameters)
#Parameters is the parameter (synapse/weight) count of the given neural network, i.e., the number of elements in the weight tensors.

## Slide 56: Number of Parameters (#Parameters)
y2
y1
y0
x4
x3
x0 x1 x2
w
00
w
42
co
ci
=
co
WT
X
Y
ci
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh, kw | Kernel Height/Width
g | Groups

## Slide 57: Number of Parameters (#Parameters)
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh, kw | Kernel Height/Width
g | Groups

## Slide 58: Number of Parameters (#Parameters)
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh, kw | Kernel Height/Width
g | Groups
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | g g
Depthwise Convolution | 
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 

## Slide 59: Number of Parameters (#Parameters)
co
c
i
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh, kw | Kernel Height/Width
g | Groups
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | g
Depthwise Convolution | 
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 

## Slide 60: AlexNet: #Parameters
66
61M in total
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | g
Depthwise Convolution | 
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 

## Slide 61: Efficiency of Neural Networks
Efficiency Metrics
Memory-Related #parameters
model size
total/peak #activations
Computation-Related
MAC
FLOP, FLOPS
OP, OPS
Faster
Smaller
Greener
Storage
Latency
Energy
Computation
Memory

## Slide 62: Model Size
Model size measures the storage for the weights of the given neural network.
  The common units for model size are: MB (megabyte), KB (kilobyte), bits.
  In general, if the whole neural network uses the same data type (e.g., floating-point),
Model Size = #Parameters ∙ Bit Width
  Example: AlexNet has 61M parameters.
If all weights are stored with 32-bit numbers, total storage will be about
  61M × 4 Bytes (32 bits) = 228 MB
If all weights are stored with 8-bit numbers, total storage will be about
  61M × 1 Bytes (32 bits) = 61 MB

## Slide 63: Efficiency of Neural Networks
Efficiency Metrics
Memory-Related #parameters
model size
total/peak #activations
Computation-Related
MAC
FLOP, FLOPS
OP, OPS
Faster
Smaller
Greener
Storage
Latency
Energy
Computation
Memory

## Slide 64: Number of Activations (#Activations)
#Activation is the memory bottleneck in inference on IoT, not #Parameters
MIT 6.5940: TinyML and Eﬃcient Deep Learning Computing

## Slide 65: Number of Activations (#Activations)
#Activation didn’t improve from ResNet to MobileNet-v2
MIT 6.5940: TinyML and Eﬃcient Deep Learning Computing

## Slide 66: Number of Activations (#Activations)
Imbalanced memory distribution of MobileNetV2

## Slide 67: Number of Activations (#Activations)
#Activation is the memory bottleneck in training, not #Parameters.

## Slide 68: Number of Activations (#Activations)
Activation and weight memory distribution of MCUNet

## Slide 69: AlexNet: #Activations
75
Total #Activation: 932,264 Peak #Activation:
≈ #input activation + #output activation
= 150,528 + 290,400 = 440,928

## Slide 70: Efficiency of Neural Networks
Efficiency Metrics
Memory-Related #parameters
model size
total/peak #activations
Computation-Related
MAC
FLOP, FLOPS
OP, OPS
Faster
Smaller
Greener
Storage
Latency
Energy
Computation
Memory

## Slide 71: Number of Multiply-Accumulate Operations
Multiply-Accumulate Operation (MAC)
  𝑎←𝑎+𝑏∙𝑐
Matrix-Vector Multiplication (MV)
  𝑀𝐴𝐶𝑠=𝑚∙𝑛
General Matrix-Matrix Multiplication (GEMM)
  𝑀𝐴𝐶𝑠=𝑚∙𝑛∙𝑘

## Slide 72: Number of Multiply-Accumulate Operations
y2
y1
y0
x4
x3
x0 x1 x2
w
00
w
42
co
ci
=
co
WT
X
Y
ci
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh, kw | Kernel Height/Width
g | Groups
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | g
Depthwise Convolution | 
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 

## Slide 73: Number of Multiply-Accumulate Operations
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh, kw | Kernel Height/Width
g | Groups
Layer | #MACs
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
Layer | #MACs
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 

## Slide 74: Number of Multiply-Accumulate Operations
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh, kw | Kernel Height/Width
g | Groups
Layer | #MACs
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
Layer | #MACs
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 

## Slide 75: Number of Multiply-Accumulate Operations
co
c
Notations | 
n | Batch Size
ci | Input Channels
co | Output Channels
wi, wo | Input/Output Width
hi, ho | Input/Output Height
kh, kw | Kernel Height/Width
g | Groups
Layer | #MACs
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
Layer | #MACs
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
ci

## Slide 76: AlexNet: #MACs
82
724M in total !!
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 
Layer | #Parameters
Linear Layer | 
Convolution | 
Grouped Convolution | 
Depthwise Convolution | 

## Slide 77: Efficiency of Neural Networks
Efficiency Metrics
Memory-Related #parameters
model size
total/peak #activations
Computation-Related
MAC
FLOP, FLOPS
OP, OPS
Faster
Smaller
Greener
Storage
Latency
Energy
Computation
Memory

## Slide 78: Number of Floating Point Operations (FLOP)
A multiply is a floating-point operation
An add is a floating-point operation
One multiply-accumulate operation is two floating-point operations (FLOPs)
  Example: AlexNet has 724M MACs, total number of floating-point operations will be
    724M x 2 = 1.4G FLOPs
Floating-Point Operations Per Second (FLOPS)

## Slide 79: Number of Operations (OP)
Activations/weights in neural network computing are not always floating-point
To generalize, number of operations is used to measure the computation amount
  Example: AlexNet has 724M MACs, total number of floating-point operations will be
    724M x 2 = 1.4G OPs
Similarly, Operations Per Second (OPS)

## Slide 80: Roofline Model for Performance Analysis

## Slide 81: Process of DNN Inference on Hardware
Memory (Off-Chip)
Caches (On-Chip)
GPU/CPU
Step 2 (Compute): Perform the operations
(e.g. Linear, Convolution…etc)
Step 1 (Memory Access): Moving Input/Weights from memory onto GPU/CPU
Step 3 (Memory Access):
Writing the computed
activation back to memory

## Slide 82: Systolic Array – Overview
Matrix multiply unit in Google Tensor Processing Unit (TPU)
Balancing computation with I/O
Simple and regular

## Slide 83: Systolic Array – Example

## Slide 84: Operational Intensity
Measure of data locality (data reuse)
Ratio of Total FLOPs performed to Total Bytes moved
Compute Intensive Operation
  High computations (usually high operational intensity)
  Example: Convolution, Fully-Connected
Memory Intensive Operation
  High memory access (usually low operational intensity)
  Example: Activation
Compute
DRAM (Off-Chip)
Caches (On-Chip)

## Slide 85: Transformer Block & Attention

## Slide 86: Performance Roofline: Memory Bandwidth
Performance is bounded by the bandwidth of memory
DRAM (Off-Chip)
Caches (On-Chip)
Operational
Intensity
FLOPs/Bytes
Attainable
Performance ()
FLOPS
Memory Bandwidth

## Slide 87: Performance Roofline: Computation Capability
Performance is bounded by the computation capability of hardware
DRAM (Off-Chip)
Caches (On-Chip)
Operational
Intensity
FLOPs/Bytes
Attainable
Performance ()
FLOPS
Peak Hardware
Performance
Compute
Bound

## Slide 88: Roofline Model
Performance roofline is bounded by “memory” or “compute”
DRAM (Off-Chip)
Caches (On-Chip)
Operational
Intensity
FLOPs/Bytes
Attainable
Performance ()
FLOPS
Memory Bandwidth
Peak Hardware
Performance
Memory
Bound
Compute
Bound

## Slide 89: Estimated Execution Time
The execution time is the number of operations divided by performance
Memory Bound
Compute Bound
Operational
Intensity
FLOPs/Bytes
Attainable
Performance ()
FLOPS
Memory
Bound
Compute
Bound

## Slide 90: Example Usage of Roofline Model
Higher Operational Intensity  Higher Hardware Utilization
Operational
Intensity
FLOPs/Bytes
Attainable
Performance ()
FLOPS
4608 GFLOPS
Bandwidth = 96 GB/s
48
2.4
(op1)
22.5
(op2)
37.7
(op3)
64
(op4)
174
(op6)
227 GFLOPS
2157 GFLOPS
3617 GFLOPS
4608 GFLOPS
4608 GFLOPS
Operation | #FLOPs (M) | #Memory Access (MB)
op1 | 57.8M | 25MB
op2 | 51.4M | 2.3MB
op3 | 925M | 25MB
op4 | 236M | 3.7MB
op5 | 172M | 1.3MB
op6 | 231M | 1.3MB
Fully utilize the computation capability of hardware (Compute Bound)
Low data reuse, dominated by memory access (Memory Bound)
132
(op5)
4608 GFLOPS

## Slide 91: Insight from Roofline Model
Reduce #Memory Access when it’s memory bound (op1 vs. op2)
  Reducing #FLOPs results in no speedup (op1 vs. op3)
  Smaller #FLOPs does not imply faster execution
Operation | #FLOPs (M) | #Memory Access (MB) | Operational Intensity | Attainable Performance (GFLOPS) | Theoretical Inference Time
op1 | 57.8M | 24.5MB | 2.4 | 226.5 | 255
op2 | 51.4M | 2.3MB | 22.5 | 2156.7 | 23.8
op3 | 925M | 24.5MB | 37.7 | 3622.6 | 255

## Slide 92: Insight from Roofline Model
Reduce #FLOPs when it’s compute bound (op5 vs. op6)
  Reducing #Memory Access results in no speedup (op4 vs. op6)
  Smaller #Memory Access does not imply faster execution
Operation | #FLOPs (M) | #Memory Access (MB) | Operational Intensity | Attainable Performance (GFLOPS) | Theoretical Inference Time
op4 | 236M | 3.7MB | 64 | 4608 | 51.2
op5 | 172M | 1.3MB | 132 | 4608 | 37.3
op6 | 231M | 1.3MB | 174 | 4608 | 50.3

## Slide 93: Different Hardware Platforms, Different Rooflines
TPUv4: https://dl.acm.org/doi/pdf/10.1145/3579371.3589350

## Slide 94: Memory Wall
Memory Wall and AI: https://medium.com/riselab/ai-and-memory-wall-2cb4265cb0b8

## Slide 95: 摩爾定律 (Moore’s Law)

## Slide 96: 黃氏定律 (Huang’s Law)

## Slide 97: In Between AI Models and AI Chips – An Analogue
HW: AI chip
SW: AI model

## Slide 98: Middleware for Efficient Deep Learning
涵蓋主題
  AI accelerators (general-purpose/GPU vs. custom/xPU)
  AI compilers, system runtime (e.g., TensorRT, TensorRT-LLM)
  Pruning: unstructured vs. structured NN model compression
  Sparsity: semi-structured NN model compression
  Quantization (PTQ vs. QAT)
  Neural architecture search (NAS)
  ========
  FlashAttention(1.7K, 2022), PagedAttention(1.3K, 2023), KV-Cache (compression and quantization)
  Speculative decoding, lookahead decoding, offloading
  Efficient fine-tuning: LoRA(11.1K, 2021) and DoRA(0.2K, 2024)
  Knowledge distillation and transfer learning
  LLM re-architectured: Mixture-of-Experts, DeepSeek, Mamba(2.2K, 2023)
  Distributed training, federated learning
  On-device training, privacy-aware model customization/personalization

## Slide 99: Taiwan’s Opportunities and Advantages
Cloud
Edge
Inference
Training
AI PC
Fine-tuning/distillation
K
K
S
S
S
N
N
N
Accelerators … DeepSeek?
Compilers … DeepSeek?
Compression
Quantization
NAS
FlashAttention
KV-Cache
Speculative decoding
Efficient fine-tuning (LoRA)
Efficient distillation (Liger Kernel)
Build AI models? Perhaps.
Build AI chips? Definitely.
What kind of AI chips? xPU (flexible, adaptable, and even configurable)
Build xPU’s middleware (toolchain), some tools applicable across various xPUs
成也工具鏈！敗也工具鏈！
做自己的AI晶片，
必定需要有自己的工具鏈；
即使不做自己的AI晶片，
仍會有優化現有工具鏈的需求。
NVIDIA的工具鏈不僅完整、可靠供使用者易於操作GPU來執行AI模型，還有友善的介面(CUDA, Triton)供開發者進一步優化AI模型的執行。
你認為NVIDIA目前獨占市場的原因是硬體還是軟體（工具鏈）？